## Slide 1
Water quality monitoring for
Legionella pneumophila and E. Coli

## Slide 2
Approach to water sample extraction of bacterial cell (E. coli)
Plans (Suggested)
Pick 1 colony and resuspend in 1mL media
Take out 10 µL out of 1 mL and grow on plate at 37degC
Recalculate back the original
The remaining 1mL will be stored at 4degC for future spike in purposes.
    End goal
    Develop a simple and rapid workflow for water sample processing
    Develop a quicker and sensitive method (filtration > extraction > detection)
Notes: https://www.bio-rad.com/en-sg/sku/3578121-aquadien-bacterial-dna-extraction-purification-kit?ID=3578121
https://www.qiagen.com/us/products/discovery-and-translational-research/dna-rna-purification/dna-purification/microbial-dna/dneasy-powerwater-kit/
https://www.thermofisher.com/order/catalog/product/D211001

## Slide 3
Approach to water sample extraction of bacterial cell
Plans
Determine the limit of extraction and detection of gDNA with e coli (high to low counts)
    End goal
    Develop a simple and rapid workflow for water sample processing
    Develop a quicker and sensitive method (filtration > extraction > detection)
S1
S2
Qubit detection
Quantifiable
X
X
X
Sample with conc. falls within quantifiable range
X
X
Too low to detect
Too high to detect
(100µL of E1) Lowest E. coli counts that could be detected post extraction
Dilute and culture on agar plate, and recalculate back E1 bacterial counts in 100 µL)
2. Comparison of different extraction method
Limit of Extraction & Detection (Qubit/ nanodrop)
* qPCR detection for further diluted counts
  Grow substantial amount of E. coli (that could be detected if extracted), and compare
  1. Direct extraction from direct sample (Extraction > Detection) 2. After spike into 5mL water (Filtration > extraction > detection)
To determine
yield loss (%)
Detection
Qubit
Nanodrop
Notes: https://www.bio-rad.com/en-sg/sku/3578121-aquadien-bacterial-dna-extraction-purification-kit?ID=3578121
https://www.qiagen.com/us/products/discovery-and-translational-research/dna-rna-purification/dna-purification/microbial-dna/dneasy-powerwater-kit/
https://www.thermofisher.com/order/catalog/product/D211001

## Slide 4
Comparison of Extraction protocol overview
Bacterial Culture
Pick colony (s) into 3mL LB
Grow at 37degC, 200 rpm for ~16 hr
Volume aliquote for extraction
Treatment 1 Reagent 1+Proteinase K
56degC for 1-3 hr.
Treatment 2 Reagent 2
70degC for 10 mins.
Treatment 1
Lysis buffer 1
80degC for 10 mins.
Est. ~20-30 mins.
QIAamp DNA mini kit consumables
Bacterial gDNA Extraction: QIAamp DNA mini kit (column)
QIAamp DNA mini kit consumables
Est. ~20-30 mins.
gDNA Quantification
Nanodrop
Qubit
Bacterial gDNA Extraction: Prepared Lysis Buffer + column
* 1 heating temperature for 10 mins
*2 heating temperature for =< 75mins
1
2
1
To have substantial amount of e. coli for testing.
E Lysis buffer:
NaOH
Ethanol
EDTA
Add Ethanol
3
Notes: https://www.bio-rad.com/en-sg/sku/3578121-aquadien-bacterial-dna-extraction-purification-kit?ID=3578121
https://www.qiagen.com/us/products/discovery-and-translational-research/dna-rna-purification/dna-purification/microbial-dna/dneasy-powerwater-kit/
https://www.thermofisher.com/order/catalog/product/D211001

## Slide 5
# | Sample ID | Nanodrop Nucleic Acid (ng/µL) | 260/280 | 260/230 | Sample Type | Qubit concentration (ng/µL) | Volume eluted (µL)
 | Ext. E.Coli Plate | 0.9 | 2.52 | 16.07 | DNA | Too Low To Detect | 200
 | 220422ECQamp 1000 µL | 13.8 | 2.19 | 2.34 | DNA | 7.7 | 200
1 | 220422ECQamp 100 µL | 4.8 | 2.26 | 2.51 | DNA | 0.414 | 80
2 | 220422ECQamp 10 µL | 1.2 | 2.15 | -7.03 | DNA | 0.24 | 80
3 | 220422ECQamp 1 µL | 0.9 | -9.94 | 1.29 | DNA | Too Low To Detect | 80
4 | 220422ECQamp 0.1 µL | 1 | 14.33 | -13.6 | DNA | Too Low To Detect | 80
5 | 220422ECQamp 0.01 µL | 0.9 | 7.7 | 1.71 | DNA | Too Low To Detect | 80
6 | 220422ECQamp 0.001 µL | 0.6 | -2.77 | -0.24 | DNA | Too Low To Detect | 80
7 | 220422ECQamp 0.0001 µL | 0.5 | -0.92 | 0.89 | DNA | Too Low To Detect | 80
1 | 220422EC 100 µL | 4.6 | 2.15 | -2.31 | DNA | 0.218 | 80
2 | 220422EC 10 µL | 1.5 | 3.25 | -0.32 | DNA | Too Low To Detect | 80
3 | 220422EC 1 µL | 1.4 | 2.18 | -0.38 | DNA | Too Low To Detect | 80
4 | 220422EC 0.1 µL | 0.8 | -1.11 | -0.18 | DNA | Too Low To Detect | 80
5 | 220422EC 0.01 µL | 1.1 | 18.37 | -0.31 | DNA | Too Low To Detect | 80
6 | 220422EC 0.001 µL | 1.4 | 5.98 | -0.4 | DNA | Too Low To Detect | 80
7 | 220422EC 0.0001 µL | 1.4 | 5.77 | -0.35 | DNA | Too Low To Detect | 80
Bacterial gDNA Extraction: Prepared Lysis Buffer + column
Bacterial gDNA Extraction: QIAamp DNA mini kit (column)
Will be tested for Developed qPCR
Comparison of Extraction protocol: Nanodrop & Qubit
Nanodrop & Qubit were unable to detect extracted samples below 10 µL.
The extracted samples were tested with qPCR subsequently with the primers we have just received
Notes: https://www.bio-rad.com/en-sg/sku/3578121-aquadien-bacterial-dna-extraction-purification-kit?ID=3578121
https://www.qiagen.com/us/products/discovery-and-translational-research/dna-rna-purification/dna-purification/microbial-dna/dneasy-powerwater-kit/
https://www.thermofisher.com/order/catalog/product/D211001

## Slide 6
Comparison of Extraction protocol: qPCR detection of UidA (E. coli)
E Lysis buffer
EC 100 µL
QIAamp
E Lysis buffer
EC 10 µL
QIAamp
E Lysis buffer
EC 1 µL
QIAamp
E Lysis buffer
EC 0.1 µL
QIAamp
E Lysis buffer
EC 0.01 µL
QIAamp
E Lysis buffer
EC 0.001 µL
QIAamp
E Lysis buffer
EC 0.0001 µL
QIAamp
Note:
qPCR detection demonstrated that the extraction efficiency of E lysis protocol with reference protocol (QIAamp DNA mini kit) were comparable with ~1 ct difference.
Highest titer
Lowest titer
Notes: https://www.bio-rad.com/en-sg/sku/3578121-aquadien-bacterial-dna-extraction-purification-kit?ID=3578121
https://www.qiagen.com/us/products/discovery-and-translational-research/dna-rna-purification/dna-purification/microbial-dna/dneasy-powerwater-kit/
https://www.thermofisher.com/order/catalog/product/D211001

## Slide 7
Subsequent Plans:
Optimization of Prepared Lysis buffer
1. Temperature: RT vs 70degC (10mins) vs 80 degC (10mins) vs 90 degC (10mins)
2. Modification (Addition of detergent etc.)
Advantages of Prepared buffer protocol:
1. Flexible in modification of lysis buffer for optimization
2. Shorter duration of extraction from bacterial cells (10 mins instead of 75 mins)
3. 100 µL of sample (No need to centrifuge for pellet) can be processed directly.
4. Currently, 1 heating temperature (80 degC) as compared to reference protocol (56 & 70 degC).
Disadvantages of Prepared buffer protocol:
1. May be inefficient in extracting cell pellet with E Lysis buffer; ~50% (nanodrop)
qPCR difference
Direct Sample extraction vs Filtered Sample Extraction;
1. Syringe membrane filter (0.2um) may be used to trap Bacterial cells (I.e. E. coli) from water sample (Spiked-in samples).
2. Lysis of cells within the membrane filter using modified buffer.
3. Determine % of yield loss.
EC pellet
QIAamp
E Lysis
buffer
Notes: https://www.bio-rad.com/en-sg/sku/3578121-aquadien-bacterial-dna-extraction-purification-kit?ID=3578121
https://www.qiagen.com/us/products/discovery-and-translational-research/dna-rna-purification/dna-purification/microbial-dna/dneasy-powerwater-kit/
https://www.thermofisher.com/order/catalog/product/D211001

## Slide 8
Quantification: and cell count
Notes: https://www.bio-rad.com/en-sg/sku/3578121-aquadien-bacterial-dna-extraction-purification-kit?ID=3578121
https://www.qiagen.com/us/products/discovery-and-translational-research/dna-rna-purification/dna-purification/microbial-dna/dneasy-powerwater-kit/
https://www.thermofisher.com/order/catalog/product/D211001

## Slide 9
Commercially Available Extraction Kits for Nucleic Acid Extraction
Bio Rad - Aquadien™ Bacterial DNA Extraction and Purification Kit
Applicable for both Legionella
& E. coli Extraction
Suitable for: Bacterial DNA extraction from water samples, Aerosols & Biofilms
QIAGEN- DNeasy PowerWater Kit
Applicable for both Legionella
& E. coli Extraction
Suitable for: Bacterial DNA extraction from water samples only
Price : USD 1077
Thermo Scientific - qualyfast ® DNA Extraction kit I / II
Applicable for both Legionella
& E. coli Extraction
Suitable for: Bacterial DNA extraction from Clear/dirty water samples and sediments
Notes: https://www.bio-rad.com/en-sg/sku/3578121-aquadien-bacterial-dna-extraction-purification-kit?ID=3578121
https://www.qiagen.com/us/products/discovery-and-translational-research/dna-rna-purification/dna-purification/microbial-dna/dneasy-powerwater-kit/
https://www.thermofisher.com/order/catalog/product/D211001